## Slide 1: An Extendable DASH Streaming System for Dynamic Point Clouds
BACHELOR THESIS
PRESENTATION
Özgür Erol | Supervisor: Michael Rudolph
22.09.2022
Networks and Communication Systems | Prof. Dr. –Ing. Amr Rizk
Notes: Organizations are increasingly getting more open to the idea of point clouds.
They allow them to create realistic representations of the real world and bring
in the flexibility they need, that sets them apart from other competitors.
Point clouds are not only used in high-tech industries, but are available for the
average consumer: Due to cost-effective and accessible head-mounted displays,
the user is able to engage in immersive virtual reality applications, free from any restrictions.
Although the idea of point clouds sound promising, they are plagued
by what seems to be a reoccurent issue:
And that is their size, resulting in massive memory requirements.
Not only do they create difficulties for storage, but complicate transmission in real time.

## Slide 2
AGENDA
01.
02.
03.
04.
05.
06.
07.
Introduction
Background
Related Work
Design
Implementation
Evaluation
Conclusion
Notes: Before I go any further, allow me to give you a quick overview of my presentation.
After the introduction, I will start with the background section and provide you with
a general understanding of the idea of point clouds.
Next, I present an overview of the current state of point cloud streaming,
including the progress made in point cloud compression.
The second part of this presentation will revolve around the proposed point cloud streaming solution and
focus on design decisions and implementation details.
The evaluation section will present the results of the simulations
that we performed with the proposed system.
Finally, the last section will summarize the main findings of the thesis and present future work.

## Slide 3
Video 1 An example for a point cloud
01 | INTRODUCTION

## Slide 4: Why Point Clouds?
Rise in popularity due to the accessibility of head-mounted displays 1
Most favorable format for representing volumetric data 2
Allow the user to change viewport and position
01 | INTRODUCTION
Problem
Point clouds have immense memory requirements
Research around point cloud streaming is scarce
Contribution
An understanding of the current state of point cloud streaming
A streaming system for point clouds that supports future development
Point Clouds in Practical Use
Immersive virtual and augmented reality (VR/AR) applications 3
Mobile mapping to support autonomous driving 4
1 van der Hooft et al., 2019
2 Liu et al., 2021
3 Graziosi et al., 2020
4 Cui et al., 2019

## Slide 5
02 | POINT CLOUDS
Definition and Characteristics of Point Clouds
Each point represents a position and other additional attributes (e.g. color) 3
Acquired by photogrammetry and/or depth scanners 3,5
Two types of point clouds: dynamic and static 4
Higher point density results in a higher quality
15 211 63 61 133 104 77
16 210 63 63 128 97 69
17 211 62 63 126 97 71
18 211 63 62 130 100 73
19 211 63 63 129 98 71
20 212 63 59 139 110 83
Listing 1 An excerpt of the file content of longdress 6
Figure 1 An example for a dynamic point cloud 6, containing about 750.000 points per frame
3 Graziosi et al., 2020
4 Cui et al., 2019
5 Hosseini & Timmerer, 2018
6 d’Eon et al., 2017

## Slide 6
02 | STREAMING
Idea of Streaming
Two modes of watching a video: download mode and streaming mode 7
Streaming mode allows early playback 8 and saves storage
Adaptive Bitrate Streaming
Adjusts the video quality to the network conditions of the user 5
Requires multiple quality representations
Prevents long starting times and buffering 9
Dynamic Adaptive Streaming over HTTP (DASH)
Started with a Call for Proposals (CfP) in 2009 and evolved to an international standard 10
Uses a Media Presentation Description (MPD)
Requires the client to implement an adaptation algorithm 11
5 Hosseini & Timmerer, 2018
7 Wu et al., 2001
8 Li et al., 2013
9 Seufert et al., 2014
10 Sodagar, 2011
11 Stockhammer, 2011

## Slide 7: Point Cloud Compression
Compression methods have mainly focused on static point clouds 12
Early studies used tree data structures for compression 13,14
03 | COMPRESSION
MPEG‘s Call for Proposals (2017)
Geometry-based point cloud compression (G-PCC)
Video-based point cloud compression (V-PCC)
Used with static and dynamically acquired point clouds 12
Compression using octrees 4
Used with dynamic point clouds 4
Compression by projecting the data on two-dimensional space 15
Problem
Compression requires additional software16
Decoding in real-time is not possible1
1 van der Hooft et al., 2019
4 Cui et al., 2019
12 Schwarz et al., 2018
13 Huang et al., 2006
14 Schnabel & Klein, 2006
15 Liu et al., 2019
16 Qian et al., 2019

## Slide 8: Concept and Results of DASH-PC 5
03 | POINT CLOUD STREAMING
Create different quality representations by subsampling the point cloud
Little quality degradation, due to human visual acuity
Video 2 A demonstration of the idea of DASH-PC
Bandwidth savings up to 50-80%
1 van der Hooft et al., 2019
5 Hosseini & Timmerer, 2018
Concept and Results of PCC-DASH 1
Create different quality representations by compressing the point cloud
Rank point cloud objects and assign bandwidth according to importance
Figure 2 An example for a multi object scene
Adaptation algorithm depends on the scene
Notes: Sample: 765,000 with 16.4 MB
Subsample: 20,000 with 0.9 MB

## Slide 9
04 | THE PROPOSED SYSTEM
Idea of the Proposed System
Make point clouds available to a wide range of consumers
Combine the strengths of existing solutions
Support the development of point cloud streaming
Characteristics of the Point Cloud Streaming System
Adjusts the point cloud quality to the network conditions of the user by implementing DASH
Uses compressed point cloud files, created by V-PCC
Provides the user with the highest quality possible
Supports the creation of new methods
Provides methods for evaluating different point cloud streaming methods
Includes two adaptation algorithms
Configuration of the system
A server to store the point cloud files along with the MPDs
A client that obtains the point clouds and implements an adaptation algorithm

## Slide 10
04 | SERVER ARCHITECTURE
Contains the information for the stream
Are transmitted to the client
Required for analysing the point clouds
MPD File
Compressed Point Cloud Data
Raw Point Cloud Data
Creates the MPD file
MPD Creation Module
Contains the configuration options for the point cloud scene
Configuration File
Figure 3 The architecture of the server

## Slide 11
04 | CLIENT ARCHITECTURE
Estimates the user‘s bandwidth
Decides how the bandwidth is allocated to the ranked objects
Prevents stalls and rebuffering
Throughput Estimator
Bitrate Allocation
Buffer
Reads the MPD file
MPD Parser
Contains the configuration options for the client
Configuration File
Evaluates the performance of the system configuration
Logging & Diagram Creation
Adaptation Algorithm
Figure 4 The architecture of the client

## Slide 12
05 | CONFIGURATION
1 [basic] 2 server_url=192.168.178.73 3 manifest_filename=manifest-multi-10 4 min_buffer_size=2 5 dash_logic=basic 6 # bitrate_allocation=greedy 7 bandwidth_trace=40-wired 8 simulation=true 9 10 [print] # options: ["true"|"false"] 11 print_bandwidth=true 12 print_buffer=true 13 print_file_request=true 14 15 [log] # options: ["true"|"false"] 16 log_bandwidth=false 17 log_buffer=false 18 19 [diagram] # options: ["disable"|"show"|"save"] 20 buffer_chart=save
Listing 2 The configuration file for the client
Listing 3 The configuration file for the server
1 [basic] 2 title=Multi Point Cloud Setting 3 file_format=bin 4 type=dynamic 5 framerate=30 6 duration=1 7 pc_directory_name=point-clouds 8 representation_url=$adaptationset_name$/
$representation_id$/segment_$period_id$ 9 10 [loot] 11 rot=0 0 0 12 pos=-1400 0 0 13
14 [redandblack] 15 rot=0 0 0 16 pos=-900 0 0 17
18 [solder]
19 # ...

## Slide 13
05 | MPD
1 <?xml version='1.0' encoding='UTF-8'?> 2 <MPD format="bin" type="dynamic" mediaPresentationDuration="2" framerate="30"> 3 <RepresentationURL>point-clouds/$adaptationset_name$/$representation_id$/segment_$period_id$.bin</RepresentationURL> 4 <Period id="0"> 5 <AdaptationSet id="0" name="longdress" duration="1" pos="100 0 0" rot="0 0 0" size="103 9 22 459 1012 318"> 6 <Representation id="1" bandwidth="4511264" /> 7 <Representation id="2" bandwidth="7704904" /> 8 </AdaptationSet> 9 <AdaptationSet id="1" name="loot" duration="1" pos="-1400 0 0" rot="0 0 0" size="28 7 119 380 999 473"> 10 <Representation id="1" bandwidth="2176080" /> 11 <Representation id="2" bandwidth="3405168" /> 12 </AdaptationSet> 13 </Period> 14 <Period id="1"> 15 <AdaptationSet id="0" name="longdress" duration="1" pos="100 0 0" rot="0 0 0" size="135 6 173 460 992 496"> 16 <Representation id="1" bandwidth="4818680" /> 17 <Representation id="2" bandwidth="8202072" /> 18 </AdaptationSet> 19 <AdaptationSet id="1" name="loot" duration="1" pos="-1400 0 0" rot="0 0 0" size="28 7 134 385 1003 465"> 20 <Representation id="1" bandwidth="2332920" /> 21 <Representation id="2" bandwidth="3564968" /> 22 </AdaptationSet> 23 </Period> 24 </MPD>
Listing 4 An examplary MPD for point cloud streaming, featuring two point cloud objects

## Slide 14
05 | SYSTEM
Video 3 Demonstration of the proposed system

## Slide 15: System Configuration
06 | EVALUATION SETUP
Figure 5 Wired and wireless 17 bandwidth trace with a mean bandwidth of 80 Mbps
2x Raspberry Pi 4 Model B with 4GB of RAM running Ubuntu 22.04 LTS
Server: NGINX HTTP/1.1
Distinction between single object and multi object scenes
Two bandwidth configurations: wired and wireless
Video 4 Positioning of the point cloud objects for the multi object scene 1
1 van der Hooft et al., 2019
17 van Der Hooft et al., 2016

## Slide 16
06 | EVALUATION RESULTS
Figure 6 Average quality for (a) a single object scene and (b) a multi object scene with four objects under three different bandwidth configuration using dash basic
(a)
(b)
Results
The wired configuration produces results similar to a fixed bandwidth configuration
The bandwidth fluctuations for a wired/wireless configuration can cause a higher quality
The difference between the wired and wireless graph tends to increase for higher values for the mean bandwidth
A mean bandwidth speed of 60 Mbps for single object scenes and 140 Mps for the multi object scene is required to stream with the highest possible quality

## Slide 17
06 | EVALUATION RESULTS
Figure 7 : Distance-based adaptation algorithm, using the (a) greedy bitrate allocation scheme and the (b) uniform
bitrate allocation scheme 1
(a)
(b)
Results
The loot object has the highest average quality for small values for the mean bandwidth, while the soldier object reaches the maximum quality first
The change in average quality with the greedy bitrate allocation scheme is rather stark
The uniform bitrate allocation scheme produces more balanced results but has a lower overall quality
Balance between quality and performance: Quality switches have a great impact on the user‘s satisfaction, especially is the switches happen abruptly9
1 van der Hooft et al., 2019
9 Seufert et al., 2014

## Slide 18: Point Cloud Streaming
Adaptive bitrate streaming provides support for bandwidth-limited users
Adaptation algorithms are crucial for bandwidth savings
Wireless configurations are prone to quality degradation
07 | CONCLUSION
Initial Problem
Point cloud streaming requires high bandwidth speeds
The Proposed Point Cloud Streaming System
Evaluates the performance of point cloud streaming methods
Provides a framework for future development
Limitations and Future Work
The throughput estimation module is inaccurate
Decoding requires high processing power, making point cloud streaming impractical
Extend the findings with subjective evaluations

## Slide 19
REFERENCES
1 van der Hooft, Jeroen, et al. "Towards 6dof http adaptive streaming through point cloud compression." Proceedings of the 27th ACM International Conference on Multimedia. 2019.
2 Liu, Zhi, et al. "Point cloud video streaming: Challenges and solutions." IEEE Network 35.5 (2021): 202-209.
3 Graziosi, D., et al. "An overview of ongoing point cloud compression standardization activities: Video-based (V-PCC) and geometry-based (G-PCC)." APSIPA Transactions on Signal and Information Processing 9 (2020).
4 Cui, Li, et al. "Point-cloud compression: Moving picture experts group's new standard in 2020." IEEE Consumer Electronics Magazine 8.4 (2019): 17-21.
5 Hosseini, Mohammad, and Christian Timmerer. "Dynamic adaptive point cloud streaming." Proceedings of the 23rd Packet Video Workshop. 2018.
6 d’Eon, Eugene, et al. "8i voxelized full bodies-a voxelized point cloud dataset." ISO/IEC JTC1/SC29 Joint WG11/WG1 (MPEG/JPEG) input document WG11M40059/WG1M74006 7.8 (2017): 11.
7 Wu, Dapeng, et al. "Streaming video over the Internet: approaches and directions." IEEE Transactions on circuits and systems for video technology 11.3 (2001): 282-300.
8 Li, Baochun, et al. "Two decades of internet video streaming: A retrospective view." ACM transactions on multimedia computing, communications, and applications (TOMM) 9.1s (2013): 1-20.
9 Seufert, Michael, et al. "A survey on quality of experience of HTTP adaptive streaming." IEEE Communications Surveys & Tutorials 17.1 (2014): 469-492.
10 Sodagar, Iraj. "The mpeg-dash standard for multimedia streaming over the internet." IEEE multimedia 18.4 (2011): 62-67.
11 Stockhammer, Thomas. "Dynamic adaptive streaming over HTTP-- standards and design principles." Proceedings of the second annual ACM conference on Multimedia systems. 2011.
12 Schwarz, Sebastian, et al. "Emerging MPEG standards for point cloud compression." IEEE Journal on Emerging and Selected Topics in Circuits and Systems 9.1 (2018): 133-148.
13 Huang, Yan, et al. "Octree-Based Progressive Geometry Coding of Point Clouds." PBG@ SIGGRAPH. 2006.
14 Schnabel, Ruwen, and Reinhard Klein. "Octree-based Point-Cloud Compression." PBG@ SIGGRAPH 3 (2006).
15 Liu, Hao, et al. "A comprehensive study and comparison of core technologies for MPEG 3-D point cloud compression." IEEE Transactions on Broadcasting 66.3 (2019): 701-717.
16 Qian, Feng, et al. "Toward practical volumetric video streaming on commodity smartphones." Proceedings of the 20th International Workshop on Mobile Computing Systems and Applications. 2019.
17 Van Der Hooft, Jeroen, et al. "HTTP/2-based adaptive streaming of HEVC video over 4G/LTE networks." IEEE Communications Letters 20.11 (2016): 2177-2180.
18 Subramanyam, Shishir, et al. "User centered adaptive streaming of dynamic point clouds with low complexity tiling." Proceedings of the 28th ACM international conference on multimedia. 2020.
19 "JPEG Pleno Database: GTI-UPM Point-cloud data set", http://plenodb.jpeg.org/pc/upm. Accessed 21 September 2022
20 “GeoSLAM Point Cloud Animation | Road Data” YouTube, uploaded by GeoSLAM, 2021, www.youtube.com/watch?v=2Zpw_KAEhDY.

## Slide 20: Appendix

## Slide 21
HTTP
Benefits of Hypertext Transfer Protocol (HTTP) over Real-time Transport Protocol (RTP) 10
The internet infrastructure along with content delivery networks (CDNs) supports HTTP
HTTP requests can pass through any firewall
The server does not store session states
Which applications use HTTP for Streaming? 9
Apple‘s HTTP Live Streaming (HAS)
Adobe‘s HTTP Dynamic Streaming (HDS)
Dynamic Adaptive Streaming over HTTP (DASH)
9 Seufert et al., 2014
10 Sodagar, 2011
Notes: Client-server protocol, therefore, the requests can pass through firewalls

## Slide 22
V-PCC COMPRESSION
Idea of Video-based point cloud compression (V-PCC) 12,15
Patch Generation: By estimating the normal for each point, 3D patches are generated and projected onto a plane
Patch Packing: The patches are placed on a 2D grid, while minimizing the space
Occupance Map Generation: A binary map to examine wether a block of the 2D grid is occupied
Image Generation: The geometry and texture information is stored in 2D images
Padding: Creates a smooth transition between patches, which is beneficial for video encoding
Video Encoding: The geometry and texture images, along with the occupancy map is compressed using traditional video encoders.
12 Schwarz et al., 2018
15 Liu et al., 2019

## Slide 23: Drawbacks of 3D Meshes 15
Natural objects are difficult to reconstruct with 3D meshes
High data volume
High rendering complexity
Compression methods concentrate on computer generated objects
VOLUMETRIC DATA FORMATS
Figure 8 Example of a 3D mesh
Why choose Point Clouds? 18
Easy to acquire
Low rendering complexity
15 Liu et al., 2019
18 Subramanyam et al., 2020

## Slide 24: Types of Point Clouds
POINT CLOUDS
Figure 9 Static 19
Video 5 Dynamic 6
Figure 11 Dynamically Acquired 20
6 d’Eon et al., 2017
19 JPEG Pleno Database: GTI-UPM Point-cloud data set
20 GeoSLAM Point Cloud Animation, 2021